## Slide 1
IoT + AI FOREST PROTECTION
Forest Beacon
AI-Powered Deforestation Detection System
Real-time chainsaw detection · Alert system · IoT device mapping
Sanka Hema Naga Sri Varshith(230150023)
Mogali Pranav Kumar Reddy(230150016)
Madam Abhiram(230150015)
Bandi Kesav Sai Kalyan Ram(230150005)

## Slide 2
System Architecture
End-to-End Pipeline — From Forest Floor to Alert
🌲 IoT LAYER
ESP32 Devices
• Passive listening mode
• Loud sound → 5s clip recorded
• Suspicion check on 5s clip
• Pass? → captured 5s clip
sent to central server via Wi-Fi
⚙️ BACKEND
FastAPI + PostgreSQL
• Receives 5s audio clips
• Runs CNN prediction model
• Logs stored in PostgreSQL DB
• Audio files saved to disk
• File path referenced in DB log
📊 FRONTEND
React Dashboard
• Real-time device map (Google Maps)
• Displays all IoT device locations
• Shows detection logs & history
• Chainsaw alert notifications
• Audio playback from logs
Two-stage recording minimizes bandwidth · Central DB as single source of truth

## Slide 3
IoT Device & Audio Pipeline
ESP32 Two-Stage Capture Protocol
01
LISTEN
Device in continuous passive mode
02
DETECT
Loud sound triggers 5s recording
03
SCREEN
Suspicion criterion evaluated
04
CAPTURE
Pass? Send 5s clip
05
TRANSMIT
Clip uploaded to central server
Design Rationale
Two-stage recording reduces unnecessary data transmission. Only clips passing the suspicion criterion (5s pre-screen)
are sent to server, conserving bandwidth in remote forest deployments. Each ESP32 node operates
autonomously in listening mode, requiring no constant connectivity — only transmitting when a potential threat is detected.

## Slide 4
AI Model Architecture
Custom CNN — Mel Spectrogram Classifier
INPUT (B, 1, 64, T) — Mel Spectrogram
ConvBlock(1→32) + MaxPool2d
ConvBlock(32→64) + MaxPool2d
ConvBlock(64→128) + MaxPool2d
ConvBlock(128→256) + MaxPool2d
AdaptiveAvgPool2d → (4×4)
Dropout → Linear(4096→512) → ReLU → Dropout → Linear(512→2)
OUTPUT: Chainsaw / Other
Input Representation
Raw 5s audio → Mel Spectrogram Shape: (Batch, 1, 64, Time) 64 mel frequency bins
ConvBlock Design
Each block: Conv2d → BatchNorm → ReLU → Conv2d → BatchNorm → ReLU + MaxPool2d(2) for downsampling
Classifier Head
Dropout(0.3) for regularization 256×4×4 → 512 → 2 classes Outputs logits for cross-entropy
Alert Trigger
If predicted class = Chainsaw Server fires real-time alert Dashboard highlighted + logged

## Slide 5
Backend, Database & Dashboard
FastAPI · PostgreSQL · React · Google Maps
⚡ FastAPI Backend
Calls PyTorch CNN for inference
Writes detection log to PostgreSQL
Saves audio file to disk
Stores file path in DB record
Issues chainsaw alert if detected
🗄️ PostgreSQL Database
Logs table: device_id, timestamp
prediction, confidence score
audio_file_path (disk reference)
Devices table: location, status
Alerts table: alert_type, resolved
Index on timestamp for fast queries
🗺️ React Frontend
Google Maps: live device markers
Colour-coded by alert status
Detection log table with filters
Audio clip playback from logs
Real-time alert banner/toast
Device health / last-seen status
Chainsaw Detected → CNN flags prediction → FastAPI writes DB log → Alert fired → React dashboard highlights device on map